## Slide 1: OFDM PAPR Reduction through PTS technique

## Slide 2: Table of contents
The PAPR problem in OFDM
Theory
PAPR reduction techniques
The PTS technique
PTS simulations
Incorporation into the OFDM modem

## Slide 3: The PAPR problem in OFDM

## Slide 4: Background- OFDM
The principle: transmission of a signal that is a linear combination of an orthogonal basis
The symbols are the linear combination’s coefficients and are statistically independent:

## Slide 5: Background- OFDM
Time domain signal:
Typical shape

## Slide 6: Motivation: PA linearity
PAPR trades-off signal quality Vs. Range and Power consumption
Saturating PA causes:
  Distortion
  Loss of orthogonality (ICI)
  Spectral leakage to adjacent channels
Increasing PA’s compression point increases power consumption
Not saturation nor Increasing: compromise on Pavg, thus on Range

## Slide 7: Theory

## Slide 8: PAPR definition
For an OFDM block composed of N symbols of duration T seconds;

## Slide 9: PAPR distribution (CCDF) [1]
Central limit theorem:
Magnitude is Rayleigh distributed:
Hence;

## Slide 10: PAPR distribution (CCDF): analytic expression [1]
Probability of at least 1 sample of time domain signal to cross a certain power level:
if we define , then;

## Slide 11: PAPR distribution (CCDF): analytic expression [1]
Theoretical curves

## Slide 12: PAPR distribution –Interpolation [1]
Analog signal can be modeled by an interpolated digital signal
Interpolated digital signal has no longer uncorrelated samples
An interpolated N-samples symbol has effectively the non-interpolated PAPR of a 2N-samples symbol

## Slide 13: PAPR distribution -Interpolation
The effect of increasing the interpolation factor attains a limit
Typically, a value of L=4 is sufficient

## Slide 14: PAPR reduction techniques

## Slide 15: Criteria
PAPR reduction
BER performance
Average power conservation
Data Rate
Spectral spillage
Complexity

## Slide 16: Techniques comparison
Technique | PAPR Reduction | BER performance | Average power Conservation | Data Rate Loss | Spectral Spillage | Complexity
Clipping | 3dB | Low | Yes | None | Yes | Low
Coding[3] | 3dB | Medium | Yes | Medium | No | Low
Companding [5] | 6dB | Medium | No | None | Yes | Low
Tone Reservation | 3dB | Medium | No | High | No | High
PTS/SLM | 3dB | High | Yes | Medium | No | High

## Slide 17: Techniques comparison
Most literature ([4], [5] ,[6] and others) claims the SLM/PTS technique
tradeoffs best the different performance criteria

## Slide 18: The Partial Transmit Sequence (PTS) Technique

## Slide 19: PTS- Block Diagram

## Slide 20: Algorithm steps
Division of the N-long OFDM symbol into M sub-blocks:
  Contiguous
  Polyphase
Zero padding of each of the sub-blocks to length of N
IDFT over each of the sub-blocks
Calculation of optimum PTS coefficients vector:
  Iterative flipping
  Reduced complexity
Multiplication of the sub-blocks by the PTS coefficients
Summation of the sub-blocks

## Slide 21: Mathematical development
Frequency domain OFDM symbol vector form:
Division into M disjoint sub-blocks:
Zero padding of sub-blocks such that:
IDFT execution:

## Slide 22: Mathematical development
Multiplication by PTS coefficients:
Summation:

## Slide 23: Calculation of PTS coefficients
Optimum PTS: for every symbol, one needs to scan all possible combinations of the M coefficients and all possible values of those coefficients- impractical
In practice:
  Number of values limited to W.
  Typical values:
    W=4
    M=8
  Typical values of PTS coefficients:
    Example:
  Sub-optimal low complexity scanning algorithms

## Slide 24: Calculation of PTS coefficients- Iterative flipping [7]
b1=1
bm=1 for all m
Compute PAPR. This will be the reference PAPR
Change b2 across all possible W values:
  compute PAPR for each value
  Keep the value that brought to minimum PAPR as reference
Repeat step 2 for m=3,…,M-1

## Slide 25: Simulation

## Slide 26: Simulation (time domain)

## Slide 27: Simulation (EVM)

## Slide 28: Calculation of PTS coefficients- Reduced Complexity [4]
It is to provide very close performance in terms of PAPR reduction wrt the ideal PTS, yet with reduced complexity
Based on gradient descent search algorithm useful in combinatorial optimization problems suggested by Aarts & Lenstra
  Principle: Find gradient and optimum step simultaneously, by running over the r-distant b vectors from an initial guess. Repeat that I times

## Slide 29: Calculation of PTS coefficients- Reduced Complexity [4]
i=1
b_initial=ones(M,1). b_opt=b_initial
Run over all M-long b vectors r-Hamming away from b_opt, assign all W^r possible values and compute PAPR
Save b_opt; the one bringing to minimum the PAPR
If i<I: Increase i by 1 and return to step 3. else - terminate

## Slide 30: Expected results (vs. unmodulated, vs. ideal)
Classic
Reduced complexity
No PAPR reduction: 10.6dB

## Slide 31: Chosen set of parameters (r,I)
chosen

## Slide 32: Simulation Vs. Article
6.3 dB
5.95 dB
No PAPR reduction: 10.2dB

## Slide 33: Simulation- time domain
Notes: The peak power is the absolute one

## Slide 34: Calculation of PTS coefficients- Complexity for every OFDM symbol
  Reduced Complexity algorithm: at every i<=I
    We run over r choose M-1 different r-Hamming distant b vectors
    For every vector, we try W^r different values for the r different terms
    Conclusion:
  Iterative flipping algorithm:
  Example: I=1, M=8, W=4, r=2
    Reduced complexity: 336 steps
    Iterative flipping: 28 steps

## Slide 35: Reduced complexity Vs. Iterative flipping

## Slide 36: Incorporation into the OFDM modem

## Slide 37: Difference between article and effective signal

## Slide 38: CCDF

## Slide 39: time
W PTS
Wo PTS

## Slide 40: EVM (EsNo=40dB, no multipath)
Wo PTS
W PTS (Reduced complexity)

## Slide 41: Scrambling method

## Slide 42: References
Circuit-Aware System Design Techniques for Wireless Communication, by Everest Wang Huang
OFDM for wireless communication systems, Prasad
An Overview: Peak-to-Average Power Ratio Reduction Techniques for OFDM Signals, Jiang& Wu
PAPR Reduction of OFDM Signals Using a Reduced Complexity PTS Technique, Hee Han & Hong Lee
peak to average power ration in OFDM, Chapter 3. Shodhganga
PAPR Reduction Techniques for OFDM Systems, P.Kalaivani, ,S.R.Balasubramanian,
Peak to average power ratio reduction of an OFDM signal using PTS, Cimini, Solenberger